SDG&E Assumptions in the

PER UNIT COST GUIDE

4/1/2009

For all construction:

-Straight time work

For Substation work:

-Normal assemblies, not extra seismic additions to structures

-Used current equipment contract pricing, always subject to change

-No site development, permitting, or environmental costs included

For line construction:

EMF is 4% of total project cost before contingency

For 69kV: 1 - ACSR conductor / phase

- 20 wood equivalent steel poles per mile for single circuits

- 28 wood equivalent steel poles per mile for double circuits (accounting for Deadends)

- Rebuilds assume all poles replaced 20/20 for single circuit and 20/28 for double circuit

For higher voltages: 1- ACSR conductor / phase single circuit, 2-ACSS conductor / phase double circuit

- 6 Anchor Bolted Steel poles per mile

- 8 H - frames per mile for wood equivalent structures