Settlements & Billing

Configuration Guide: RUC Net Amount

Pre-calculation

Version 5.9

Table of Contents

1.	Purpose of Document	3

2.	Introduction	4

2.1	Background	4

2.2	Description	5

3.	Charge Code Requirements	5

3.1	Business Rules	5

3.2	Predecessor Charge Codes	9

3.3	Successor Charge Codes	9

3.4	Inputs – External Systems	9

3.5	Inputs - Predecessor Charge Codes or Pre-calculations	10

3.6	CAISO Formula	12

3.7	Outputs	15

4.	Charge Code Effective Dates	18

# Purpose of Document

The purpose of this document is to capture the requirements and design specification for a Charge Code in one document.

# Introduction

## Background

Bid Cost Recovery (BCR) is the process by which the CAISO ensures Scheduling Coordinators (SCs) are able to recover Start Up Costs (SUC), Minimum Load Costs (MLC), Transition Costs (TC), and Energy Bid Costs.  In order to recover SUC and MLC, a Generating Unit, Pumped-Storage Unit, or resource-specific System Resource must be committed by the CAISO.  Likewise, the CAISO must commit a Multi-Stage Generating Resource in order for it to receive TC compensation. Bid Cost recovery for Energy and Ancillary Services (A/S) Bids applies to Bid Cost Recovery Eligible Resources in general (for example, Generating Units, Pumped-Storage Units, Proxy Demand Resources, and System Resources) scheduled or dispatched by CAISO, independent of whether they are CAISO-committed or instead are self-committed.

For purposes of determining BCR eligibility, CAISO uses a concept called Commitment Period.  A Commitment Period consists of the consecutive time periods within a Trading Day when a resource is on-line, synchronized to the grid, and available for dispatch.  A Commitment Period is comprised of two distinct sub-types --- Self-Commitment Period and CAISO Commitment Period.  The portion of a Commitment Period where a resource submits an Energy Self-Schedule or A/S self-provision is called a Self-Commitment Period.  A Self-Commitment Period may include time periods when a resource is not operating pursuant of an Energy Self-Schedule or A/S self-provision, but must be on due to Ramping Constraints or a minimum up time or minimum down time requirement.  Resources are not eligible for BCR of SUC, MLC or TC during Self-Commitment Periods, but are eligible for BCR of awarded Energy and A/S.  The portion of a Commitment Period that is not a Self-Commitment Period is called CAISO Commitment Period.  Resources are eligible to receive BCR for SUC, MLC, TC, awarded Energy and A/S during a CAISO Commitment Period.

For each resource, the total SUC, MLC, TC, Bid Costs together with the energy and AS bid costs, and market revenues from RUC, and RTM are netted together for each Settlement Interval.  If the difference between the total costs and the market revenues is positive in the relevant market, then the net amount represents a Shortfall.  If the difference is negative in the relevant market, the net amount represents a Surplus.  For each resource or, in the case of a MSS entity that has elected net settlement, all MSS resources collectively, the RUC, and RTM Shortfalls and Surpluses are then netted over all hours of a Trading Day.  Net Surpluses from either of the RUC or RTM markets offset any net shortfalls from the RTM or RUC market, respectively, over the entire Trading Day.  If the net Trading Day amount is positive (a Shortfall), the Scheduling Coordinator receives a BCR Uplift Payment equal to the net Trading Day amount.

Bid Cost Recovery for resource costs in the IFM, RUC and RTM markets is determined for each Settlement Interval based upon a resource’s performance and delivered energy relative to its Expected Energy. Pre-calculation RUC Net Amount, as described herein, provides the net Shortfall or Surplus for the RUC component of Bid Cost Recovery.

## Description

For each Settlement Interval, this pre-calculation will generate the RUC Bid Costs, RUC Market Revenue, and the RUC Net Amount as the net difference between RUC costs and RUC revenue for Bid Cost Recovery Eligible Resources that participate in the RUC market.  The RUC Net Amount is subsequently used as an input for CC 6620, RUC and RTM Bid Cost Recovery Settlement and for Pre-calculation Bid Cost Recovery Sequential Netting.

RUC Bid Costs and RUC Market Revenue for a resource are set to zero in a Settlement Interval where the negative Uninstructed Imbalance Energy (UIE) is in excess of both (a) 5MWh divided by the number of Settlement Intervals in a Trading Hour and (b) 3% of the resource’s maximum capacity divided by the number of Settlement Intervals in a Trading Hour.

For MSS entities that have elected gross settlement, RUC Bid Cost Recovery Amount is calculated the same as non-MSS entities.  For MSS entities that have elected net settlement, RUC Bid Costs and RUC Market Revenue are calculated at the MSS level.

# Charge Code Requirements

## Business Rules

| Bus Req ID | Business Rule |
| --- | --- |
|  | This Pre-calc is a daily computation generating results on a Settlement Interval basis. |
|  | Regardless of Resource Type, RUC Net Amount must follow the same sign convention --- positive RUC Net Amount indicates a Shortfall, negative RUC Net Amount indicates a Surplus. |
|  | For purposes of determining the RUC Unrecovered Bid Cost Uplift Payments and for the purposes of allocating Net RUC Bid Cost Uplift, the CAISO shall calculate the RUC Bid Cost Shortfall or the RUC Bid Cost Surplus as the algebraic difference between the RUC Bid Cost and the RUC Market Revenues for each Bid Cost Recovery Eligible Resource for each Settlement Interval. |
|  | The RUC Bid Costs shall be calculated pursuant to Tariff Section 11.8.3.1 and the RUC Market Revenues shall be calculated pursuant to Tariff Section 11.8.3.2. |
|  | Bid Cost Recovery costs related to the energy delivered from Short Start Units committed in Real-Time as a result of awarded RUC Capacity will be included in RTM Compensation Costs. |
|  | For an MSS Operator that has elected net Settlement, regardless of other MSS optional elections (Load following or RUC opt-in or out), the RUC Bid Costs and RUC Market Revenue are combined with RTM Bid Cost and RTM Market Revenue on an MSS level. |
|  | For MSS entities that have elected net Settlement regardless of other MSS optional elections (i.e., Load following or not, or RUC opt-in or out), unlike non-MSS resources, the RUC and RTM Bid Cost Shortfall or Surplus is treated at the MSS level and not at the resource specific level, and is calculated as the RUC and RTM Bid Cost Shortfall or Surplus of all BCR Eligible Resources within the MSS. |
|  | The RUC and RTM Bid Cost Shortfall and Surplus for Energy, RUC Availability and Ancillary Services are first calculated separately for the MSS for each Settlement Interval of the Trading Day, with qualified Start-Up Cost, qualified Minimum Load Cost and qualified Multi-Stage Generator transition cost included into the RUC and RTM Bid Cost Shortfalls and Surpluses of Energy calculation. |
|  | The MSS’s overall RUC and RTM Bid Cost Shortfall or Surplus is then calculated as the algebraic sum of the RUC and RTM Bid Cost Shortfall or Surplus for Energy, the RUC Bid Cost Shortfall or Surplus for RUC Availability, and the RTM Bid Cost Shortfall or Surplus for AS for each Settlement Interval. |
|  | For any Settlement Interval, the RUC Market Revenue for a Bid Cost Recovery Eligible Resource is the RUC Availability Payment divided by the number of Settlement Intervals in a Trading Hour. |
|  | If the RUC Availability Bid Cost of a BCR Eligible Resource is reduced to zero (0) in a Settlement Interval because of Uninstructed Deviation, then the RUC Market Revenue for that resource for that Settlement Interval shall also be set to zero (0) since the resource is subject to rescission of RUC Availability Payments. |
|  | Non-Dynamic System Resources and Resource-Specific System Resources are considered to be outside the MSS; therefore, system resources will settle on a resource basis at the relevant RUC Price regardless of net or gross election. |
|  | For Multi-Stage Generating (MSG) Resources, Energy Bid Costs (determined under IFM Net Amount Pre-calculation, RUC Net Amount Pre-calculation, and RTM Net Amount Pre-calculation) are calculated at the resource level. |
|  | For Multi-Stage Generating (MSG) Resources, the comparison of market revenues to bid costs occurs at the resource level. |
|  | The Minimum Load Cost for the applicable Settlement Interval shall be the Minimum Load Cost of the Bid Cost Recovery Eligible Resource divided by the number of Settlement Intervals in a Trading Hour. |
|  | For each Settlement Interval, only the RUC Minimum Load Cost in a CAISO RUC Commitment Period is eligible for Bid Cost Recovery. |
|  | The RUC Minimum Load Cost for any Settlement Interval is zero if: |
|  | the Bid Cost Recovery Eligible Resource is manually pre-dispatched under an RMR Contract or the resource is flagged as an RMR Dispatch in the Day-Ahead Schedule in that Settlement Interval; |
|  | the Bid Cost Recovery Eligible Resource is not committed or Dispatched in the Real-time Market in the applicable Settlement Interval; or |
|  | the applicable Settlement Interval is included in an IFM Commitment Period. |
|  | For the purposes of determining RUC Minimum Load Cost for a Bid Cost Recovery Eligible Resource recovery of the RUC Minimum Load Costs is subject to the Real-time Performance Metric. |
|  | The RUC Minimum Load calculation shall be subject to the Shut-Down State Variable. |
|  | The CAISO will adjust the RTM Energy Bid Cost, the RUC and RTM Minimum Load Costs and the RTM Market Revenues calculations by multiplying the Real-Time Performance Metric with those amounts for the applicable Settlement Interval. |
|  | In all cases, regardless of the rules specified herein, the application of the Real-Time Performance Metric shall never increase a BCR Eligible Resource’s Unrecovered Bid Cost Uplift payments. |
|  | If the RTM Energy Bid Cost plus the RUC and RTM Minimum Load Costs, and the RTM Market Revenues are greater than or equal to zero (0), the CAISO will apply the Real-Time Performance Metric to RTM Energy Bid Costs, RUC and RTM Minimum Load Costs, and not the RTM Market Revenues. |
|  | If the RTM Energy Bid Costs plus the RUC and RTM Minimum Load Costs are greater than or equal to zero (0) and the RTM Market Revenues are negative, the CAISO will apply the Real-Time Performance Metric to the RTM Energy Bid Costs, RUC and RTM Minimum Load Costs, and the RTM Market Revenues. |
|  | If the RTM Energy Bid Costs plus the RUC and RTM Minimum Load Costs are negative, and the RTM Market Revenues are greater than or equal to zero (0) , the CAISO will not apply Real-Time Performance Metric to the RTM Energy Bid Costs, RUC or RTM Minimum Load Costs or the RTM Market Revenues. |
|  | If the RTM Energy Bid Costs plus the RUC and RTM Minimum Load Costs, and the RTM Market Revenues are negative, the CAISO will apply the Real-Time Performance Metric to the RTM Market Revenues but not the RTM Energy Bid Costs or the RUC or RTM Minimum Load Costs. |
|  | If for a given Settlement Interval the absolute value of the resource’s Metered Energy, less Regulation Energy and less Expected Energy, is less than or equal to the Performance Metric Tolerance Band, then the CAISO will not apply the Real-Time Performance Metric to the calculation of the RTM Energy Bid Cost, RTM Minimum Load Cost, or RTM Market Revenue. |
|  | Bid Cost Recovery (BCR) Eligible Resources are those resources eligible to participate in the Bid Cost Recovery. They include Generating Units, System Units, System Resources with RTM Economic bids, Participating Loads, and Proxy Demand Resources. (Fact) |
|  | A System Resource that has a Schedule that results from Bids submitted in violation of Section Tariff 30.5.5 (Scheduling Sourcing/Sinking in Same Balancing Authority Area) shall not be a Bid Cost Recovery Eligible Resource for any Settlement Interval that occurs during the time period covered by the Schedule that results from Bids submitted in violation of Section Tariff 30.5.5. |
|  | Accepted Self-Schedule Hourly Blocks, cleared Economic Hourly Block Bids, and cleared Economic Hourly Block Bids with Intra-Hour Option are not eligible to participate in Bid Cost Recovery in the Real-Time Market. |
|  | Scheduling Coordinators for Non-Generator Resources are not eligible to recover Start-Up Costs, Minimum Load Costs, Pumping Costs, Pump Shut-Down Costs, or Transition Costs but are eligible to recover Energy Bid Costs, RUC Availability Payments and Ancillary Service Bid Costs. |
|  | PTB Logic apples to the RUC Net Amount Pre-calculation. |
|  | Balancing Authority Area attribute shall be associated with the net amounts - for resource and MSS level net amounts - to be used in successor charge codes. |
|  | When an eligible resource has an interval with a negative MWh meter, CAISO will not charge for the energy of those intervals. |

## Predecessor Charge Codes

Charge Code/ Pre-calc Name

Pre-calc – Metered Energy Adjustment Factor

Pre-calc – IFM Net Amount

Pre-calc – RT Energy Quantity

Pre-calc – RTM Net Amount

Pre-calc – RUC No Pay Quantity

Pre-calc – Start Up and Minimum Load Cost

CC 6800 – DA RUC Availability Settlement

CC 6824 – No Pay Residual Unit Commitment (RUC) Settlement

## Successor Charge Codes

Charge Code/ Pre-calc Name

CC 6620 – RUC and RTM Bid Cost Recovery Settlement

Pre-calc – Bid Cost Recovery Sequential Netting

## Inputs – External Systems

| Row # | Variable Name | Description |
| --- | --- | --- |
| 1 | RUCAwardedQty BrtuT’I’M’VL’W’R’F’S’mdh | The Awarded RUC MW quantity above minimum load that is eligible for RUC payment. |
| 2 | RUCAcceptedBidPrice BrtuT’I’M’VL’W’R’F’S’mdh | The RUC Accepted Bid price for Business Associate and Resource r and Trading Hour h. |
| 3 | BAHourlyResourceRUCPrice BrtuT’I’M’VL’W’R’F’S’mdh | The RUC marginal price for Resource rand Trading Hour h. |
| 4 | GeneratorToleranceBandMW | Tolerance Band expressed in terms of MW capacity for Bid Cost Recovery Eligible Resources (5 MW). This value shall be stored as standing data. |
| 5 | GeneratorToleranceBandPercent | Tolerance Band for performance requirement expressed as a percentage applied to Maximum Operating Limit of a Bid Cost Recovery Eligible Resource (3%). This value shall be stored as standing data. |
| 6 | MaxOperMW BrtF’S’md | Maximum Operating MW Limit as registered in MasterFile for Business Associate B, Resource r, Resource Type t, Entity Component Type F’, Entity Component Subtype S’, and Trading Day d. Applicable for Bid Cost Recovery Eligible Resources. |

## Inputs - Predecessor Charge Codes or Pre-calculations

| Row # | Variable Name | Predecessor Charge Code/ Pre-calc Configuration |
| --- | --- | --- |
|  | BASettlementIntervalResourceRTPerformanceMetric BrtuT’I’M’F’S’mdhcif | Pre-calc – Metered Energy Adjustment Factor |
|  | TotalExpectedEnergyFiltered BrtuT’I’M’F’S’mdhcif | Pre-calc – Metered Energy Adjustment Factor |
|  | ResourceToBAAMapFactor BruT’I’Q’M’F’md | Pre-calc – Metered Energy Adjustment Factor |
|  | MSSToBAAMapFactor BT’I’Q’M’md | Pre-calc – Metered Energy Adjustment Factor |
|  | SettlementIntervalRealTimeUIE BrtuT’I’Q’M’F’S’mdhcif | Pre-calc – Real Time Energy Quantity |
|  | EligibleRUCSUC BrtuT’I’M’F’S’mdhcif | Pre-calc – Start Up and Minimum Load Cost |
|  | AvailableRUCMLC BrtuT’I’M’F’S’mdhcif | Pre-calc – Start Up and Minimum Load Cost |
|  | EligibleRUCTC BrtuT’I’M’F’S’mdhcif | Pre-calc – Start Up and Minimum Load Cost |
|  | BA5mResourceRUCNoPayBidCapacityRescissionQuantity BrtT’uI’M’R’W’F’S’VL’mdhcif | Pre-calc – RUC No Pay Quantity |
|  | BAHourlyResourceCircularScheduleFlag BrtF’S’mdh | Pre-calc – IFM Net Amount |
|  | RTMEnergyBidCostforRUCMLC BrtuT’I’M’F’S’mdhcif | Pre-calc – RTM Net Amount |
|  | RUCAvailabilitySettlementAmount BrtuT’I’M’F’S’h | CC 6800 – DA RUC Availability Settlement |
|  | NoPayRUCSettlementAmount BrtuT’I’M’F’S’mdh | CC 6824 – No Pay Residual Unit Commitment (RUC) Settlement |
|  | ResourceWholesaleExemptionFlag rmdhcif | Pre-calc Real Time Energy Quantity |

## CAISO Formula

BAARUCNetAmount BruT’I’Q’M’F’mdhcif =

RUCNetAmount BruT’I’M’F’mdhcif

Where ResourceToBAAMapFactor BruT’I’Q’M’F’md   exists

RUCNetAmount BruT’I’M’F’mdhcif =

( ( 1 – BAHourlyResourceCircularScheduleFlag BrtF’S’mdh ) * ( RUCCost BrtuT’I’M’F’S’mdhcif – RUCRevenue BrtuT’I’M’F’S’mdhcif ) )

Where

Energy Settlement Type (I’) <> ‘Net’

Note:

In design the hourly quantity BAHourlyResourceCircularScheduleFlag BrtF’S’mdh must be duplicated for each Settlement Interval.

Where RUCCost BrtuT’I’M’F’S’mdhcif =

BASettlementIntervalResourceRUCBidCostAmount BrtT’uI’M’F’S’mdhcif + BASettlementIntervalResourceEligibleRUCCommitmentCost BrtuT’I’M’F’S’mdhcif

Where BASettlementIntervalResourceEligibleRUCCommitmentCost BrtuT’I’M’F’S’mdhcif =

EligibleRUCSUC BrtuT’I’M’F’S’mdhcif +

EligibleRUCMLC BrtuT’I’M’F’S’mdhcif  +

EligibleRUCTC BrtuT’I’M’F’S’mdhcif

EligibleRUCMLC BrtuT’I’M’F’S’mdhcif =

IF

TotalExpectedEnergyFiltered BrtuT’I’M’F’S’mdhcif = 0

THEN

EligibleRUCMLC BrtuT’I’M’F’S’mdhcif = 0

ELSE IF

RTMEnergyBidCostforRUCMLC BrtuT’I’M’F’S’mdhcif > 0

THEN

EligibleRUCMLC BrtuT’I’M’F’S’mdhcif =

AvailableRUCMLC BrtuT’I’M’F’S’mdhcif *  BASettlementIntervalResourceRTPerformanceMetric BrtuT’I’M’F’S’mdhcif

ELSE

EligibleRUCMLC BrtuT’I’M’F’S’mdhcif =

AvailableRUCMLC BrtuT’I’M’F’S’mdhcif

END IF

BASettlementIntervalResourceRUCBidCostAmount BrtT’uI’M’F’S’mdhcif =

( Max ( 0, RUCAvailabilityBidCost BrtuT’I’M’F’S’mdhcif -

RUCNoPayCost BrtuT’I’M’F’S’mdhcif ) *

RUCToleranceBandEligiblityFlag BrtuT’I’M’F’S’mdhcif)

Where RUCAvailabilityBidCost BrtuT’I’M’F’S’mdhcif =

( RUCAwardedQty BrtuT’I’M’VL’W’R’F’S’mdh *

RUCAcceptedBidPrice BrtuT’I’M’VL’W’R’F’S’mdh ) / 12

And Where RUCNoPayCost BrtuT’I’M’F’S’mdhcif =

(BA5mResourceRUCNoPayBidCapacityRescissionQuantity BrtT’uI’M’R’W’F’S’VL’mdhcif *

RUCAcceptedBidPrice BrtuT’I’M’VL’W’R’F’S’mdh

RUCToleranceBandEligiblityFlag BrtuT’I’M’F’S’mdhcif =

IF

( SettlementIntervalRealTimeUIEforRUCCalc BrtuT’I’M’F’S’mdhcif < 0

AND

ABS ( SettlementIntervalRealTimeUIEforRUCCalc BrtuT’I’M’F’S’mdhcif  )

>

RUCToleranceBandQuantity BrtuT’I’M’F’S’mdhcif)

OR

ResourceWholesaleExemptionFlag rmdhcif = 1

THEN

RUCToleranceBandEligiblityFlag BrtuT’I’M’F’S’mdhcif = 0

ELSE

RUCToleranceBandEligiblityFlag BrtuT’I’M’F’S’mdhcif = 1

END IF

Where SettlementIntervalRealTimeUIEforRUCCalc BrtuT’I’M’F’S’mdhcif =

SettlementIntervalRealTimeUIE BrtuT’I’Q’M’F’S’mdhcif

And Where RUCToleranceBandQuantity BrtuT’I’M’F’S’mdhcif =

(

Max (GeneratorToleranceBandMW ,

(MaxOperMW BrtF’S’md * GeneratorToleranceBandPercent) )/12 )

Where Exists

RUCAwardedQty BrtuT’I’M’VL’W’R’F’S’mdh

Where RUCRevenue BrtuT’I’M’F’S’mdhcif =

Max (0 , RUCAvailabilityRevenue BrtuT’I’M’F’S’mdhcif -

RUCNoPayRevenue BrtuT’I’M’F’S’mdhcif ) *

RUCToleranceBandEligiblityFlag BrtuT’I’M’F’S’mdhcif

Where RUCAvailabilityRevenue BrtuT’I’M’F’S’mdhcif =

(-1)*(RUCAvailabilitySettlementAmount BrtuT’I’M’F’S’h) /12

##### And where RUCNoPayRevenue BrtuT’I’M’F’S’mdhcif =

(NoPayRUCSettlementAmount BrtuT’I’M’F’S’mdh) /12

BAARUCMSSNetBCRAmount BT’I’Q’M’mdhcif =

RUCMSSNetBCRAmount BT’I’M’mdhcif

Where MSSToBAAMapFactor BT’I’Q’M’md   exists.

RUCMSSNetBCRAmount BT’I’M’mdhcif =

MSSNetRUCCost BT’I’M’mdhcif – MSSNetRUCRevenue BT’I’M’mdhcif

Where MSSNetRUCCost BT’I’M’mdhcif =

RUCCost BrtuT’I’M’F’S’mdhcif

Where T’ = MSS and I’ = NET

And where MSSNetRUCRevenue BT’I’M’mdhcif =

RUCRevenue BrtuT’I’M’F’S’mdhcif

Where T’ = MSS and I’ = NET

## Outputs

| Output Req ID | Name | Description |
| --- | --- | --- |
|  | In addition to any outputs listed below, all inputs shall be included as outputs. |  |
|  | BAARUCNetAmount BruT’I’Q’M’F’mdhcif | RUCNetAmount associated to its BAA. |
|  | RUCNetAmount BruT’I’M’F’mdhcif | The net difference (in $) of RUC Cost and RUC Revenue for a given resource and Settlement Interval. |
|  | RUCCost BrtuT’I’M’F’S’mdhcif | The eligible bid costs (in $) associated with RUC including the Start Up Costs, Minimum Load Costs, Transition Costs, and Energy Bid Costs for a given resource and Settlement Interval. |
|  | BASettlementIntervalResourceEligibleRUCCommitmentCost BrtuT’I’M’F’S’mdhcif | The RUC CAISO-commitment costs (in $) that are eligible for Bid Cost Recovery in a given Settlement Interval. They include any applicable Start Up Cost, Minimum Load Cost or Transition Cost. |
|  | EligibleRUCMLC BrtuT’I’M’F’S’mdhcif | Pre-calc – Start-up and Minimum Load Cost Eligible RUC Minimum Load Costs for a given resource and Settlement Interval. |
|  | BASettlementIntervalResourceRUCBidCostAmount BrtT’uI’M’F’S’mdhcif | The RUC Availability Bid Cost (in $) for a given Settlement Interval, netted with cost attributed to no pay capacity and multiplied by the RUC Tolerance Band Eligibility flag to qualify the bid cost with the resource’s performance based on its negative UIE. |
|  | RUCAvailabilityBidCost BrtuT’I’M’F’S’mdhcif | The RUC Availability Bid Cost (in $) for a given resource and Settlement Interval. |
|  | RUCNoPayCost BrtuT’I’M’F’S’mdhcif | The RUC No Pay amount (in $) based upon RUC bid price for a given resource and Settlement Interval. |
|  | RUCToleranceBandEligiblityFlag BrtuT’I’M’F’S’mdhcif | An output flag (Boolean – 0/1) that indicates whether (1) or not (0) RT UIE quantity is negative and exceeds tolerance quantity for a given resource and Settlement Interval. |
|  | SettlementIntervalRealTimeUIEforRUCCalc BrtuT’I’M’F’S’mdhcif | Real-Time UIE value used in the calculation for RUC tolerance band eligibility flag. |
|  | RUCToleranceBandQuantity BrtuT’I’M’F’S’mdhcif | Settlement IntervalRUC tolerance band quantity (in MWh) that the magnitude of negative Real-Time UIE shall not exceed in order for the RUC availability bid cost and revenue to be eligible for participation in the RUC BCR calculation. |
|  | RUCRevenue BrtuT’I’M’F’S’mdhcif | The eligible RUC revenue (in $) for a given resource and Settlement Interval. |
|  | RUCAvailabilityRevenue BrtuT’I’M’F’S’mdhcif | The RUC Availability revenue (in $) for a given resource and Settlement Interval. |
|  | RUCNoPayRevenue BrtuT’I’M’F’S’mdhcif | The RUC No Pay amount (in $) based upon RUC Price for a given resource and Settlement Interval. |
|  | BAARUCMSSNetBCRAmount BT’I’Q’M’mdhcif | RUCMSSNetBCRAmount associated to its BAA. |
|  | RUCMSSNetBCRAmount BT’I’M’mdhcif | The difference (in $) between of RUC Cost and the RUC Revenue for a given net-settled MSS entity and Settlement Interval. |
|  | MSSNetRUCCost BT’I’M’mdhcif | The eligible bid costs (in $) associated with RUC including the Start Up Costs and Minimum Load Costs for a given net-settled MSS entity and Settlement Interval. |
|  | MSSNetRUCRevenue BT’I’M’mdhcif | The eligible RUC revenue (in $) for a given net-settled MSS entity and Settlement Interval. |

# Charge Code Effective Dates

| Charge Code/ Pre-calc Name | Document Version | Effective Start Date | Effective End Date | Version Update Type |
| --- | --- | --- | --- | --- |
| Pre-calc RUC Net Amount | 5.0 | 04/01/09 | 01/31/09 | Documentation Edits Only |
| Pre-calc RUC Net Amount | 5.1 | 02/01/10 | 07/31/10 | Documentation and Configuration Edits |
| Pre-calc RUC Net Amount | 5.1a | 08/01/10 | 09/30/10 | Documentation Edits Only |
| Pre-calc RUC Net Amount | 5.2 | 10/01/10 | 03/31/12 | Documentation and Configuration Edits |
| Pre-calc RUC Net Amount | 5.3 | 04/01/12 | 01/31/13 | Documentation and Configuration Edits |
| Pre-calc RUC Net Amount | 5.4 | 02/01/13 | 04/30/14 | Documentation and Configuration Edits |
| Pre-calc RUC Net Amount | 5.5 | 05/01/14 | 9/30/14 | Documentation and Configuration Edits |
| Pre-calc RUC Net Amount | 5.6 | 10/01/14 | 10/31/16 | Configuration Impacted |
| Pre-calc RUC Net Amount | 5.7 | 11/01/16 | 10/31/17 | Documentation and Configuration Edits |
| Pre-calc RUC Net Amount | 5.8 | 11/01/17 | 9/30/20 | Configuration Impacted |
| Pre-Calc RUC Net Amount | 5.9 | 10/1/20 | Open | Configuration Impacted |