LSA COMMENTS ON CAISO DRAFT ORDER 764 TARIFF LANGUAGE

LGIA

8.4 	Provision of Data from a Variable Energy Resource.  The Interconnection Customer whose Generating Facility is a Variable Energy Resource shall provide meteorological and forced outage data to the CAISO to the extent necessary for the CAISO’s development and deployment of power production forecasts for that class of Variable Energy Resources.

The Interconnection Customer with a Variable Energy Resource having wind as the energy source, at a minimum, will be required to provide the CAISO with site-specific meteorological data including: temperature, wind speed, wind direction, and atmospheric pressure.

The Interconnection Customer with a Variable Energy Resource having solar as the energy source, at a minimum, will be required to provide the CAISO with site-specific meteorological data including: temperature, atmospheric pressure, and irradiance.

The CAISO and Interconnection Customer whose Generating Facility is a Variable Energy Resource shall mutually agree to any additional meteorological data that are required for the development and deployment of a power production forecast.

The Interconnection Customer whose Generating Facility is a Variable Energy Resource also shall submit data to the CAISO regarding all forced outages to the extent necessary for the CAISO’s development and deployment of power production forecasts for that class of Variable Energy Resources.

The exact specifications of the meteorological and forced outage data to be provided by the Interconnection Customer to the CAISO, including the frequency and timing of data submittals, shall be made taking into account the size and configuration of the Variable Energy Resource, its characteristics, location, and its importance in maintaining generation resource adequacy and transmission system reliability in its area.

All requirements for meteorological and forced outage data must be commensurate with the power production forecasting employed by the CAISO.

Such requirements for meteorological and forced outage data are set forth in Appendix C, Interconnection Details, of this LGIA as they may change from time to time.

Appendix A

- Variable Energy Resource

A device for the production of electricity that is characterized by an Energy source that: (1) is renewable; (2) cannot be stored by the facility owner or operator; and (3) has variability that is beyond the control of the facility owner or operator.

# Comments

The specifics are already covered in more detail in the tariff and BPMs.  What is the purpose of stating them here?

Ditto.

This sentence just doesn’t make any sense – the IC must “agree” to additional data that are “required?”  Does this mean that the IC can say no?

In the tariff/BPMs, the requirements are given, and there is no “agreement” necessary or secret requirements that are not included there.

This sentence implies that additional requirements, beyond those in the tariff/BPMs, might be imposed.  If the CAISO wants to broaden the requirements for certain situations or kinds of VERs, it should use the regular process to alter the tariff /BPM requirements – including a stakeholder process – and not provide for imposition of additional requirements through the LGIA.

Again, the forced-outage reporting requirements are in the tariff, and you don’t need to repeat here that the project has to comply with the tariff.  Is the implication that requirements above those in the tariff might be imposed?  Also, there are no “classes” of VERs with respect to outage reporting.

REALLY troubling.  Again, it implies that requirements in addition to those in the tariff/BPMs could be imposed on a case-by-case basis based on vague criteria, and there is no language here that these requirements (as opposed to those two paragraphs up) have to be “mutually agreed” to.

What does this mean?  What specific requirements would there be beyond those in the tariff/BPMs?

Why is this needed if the requirements are already in the tariff/BPMs?

Also, how can requirements be included here if they “may change from time to time?”  Would all the LGIAs have to be amended when the requirements change?

What are the implications for Solar Thermal projects, which can provide a measure of storage, or VERs with on-site storage?

Almost all VERs – especially newer resources – can control variability in the downward direction, and some (e.g., solar thermal, or those producing below their capability at a given time) can be flexible up as well.  What is the purpose of this criterion?